## Slide 1
Contingency Stocks Updates - 2025
Partners reported stocks within their custody (along with the stocks received from AFAs)
IOM UNHCR and UNICEF have reported the stocks that they have in their own custody
BDRCS, DPHE : Non JRP Partner
Key points:

## Slide 2
Available Stocks for Partners
(Quantity available physically in the partner or stored centrally)
Source: WASH Partners, as of April 27, 2025
SL No | Stockpile of key WASH Items | Specification | UNIT | Total | Number of household covered in case of emergency | Number of beneficiaries covered in case of emergency | Remarks
1 | Hygiene kit/ 72-hour emergency kit | 1 kit/HH (avg. 5 indv.) | No. | 14,064 | 14,064 | 70,320 | 6% HHs will be covered
2 | MHM Kit | 1 kit/ women & girls in reproductive age | No. | 39,890 | - | 39,890 | 18% HHs will be covered 72-hour emergency kit (which include MHM items) Targeted: 308,000 Individuals
3 | Laundry Soap (125 - 150 gm) | 1 soap/ Person | Million | 0.3 | 59,417 | 297,086 | 27% HHs will be covered
4 | Bathing Soap (100 - 125 gm) | 1 soap/ Person | Million | 0.6 | 116,811 | 584,054 | 53% HHs will be covered
5 | Aqua tab (33 mg) | 200/HH for 15 days | Million | 12.3 | 61,664 | 308322 | 28% HHs will be covered for 15 days
6 | Jerry Can (10L) | 2/HH | No. | 27,699 | 13,850 | 27,699 | 6% HHs will be covered
7 | Water tank/bladder | 7.5L/person | m3 | 370 | 9,867 | 49,333 | 4% HHs will be covered (everyday)
8. Calcium hypochlorite, HTH, 65-70%: 3.8 tons. (existing 298 number of water networks can be distributed chlorinated water for one and half month)
9. Aluminium Sulftate - Al₂(SO₄)₃: 550kg ,
10.Tarpaulin: 1500 emergency latrines/bathing facilities will be covered
11. Desludging/Dewatering Pumps: 49
12. Chlorinating sprayers: 153, Tapstand: 49 unit

## Slide 3
Emergency Response Assessment: Fire

## Slide 4
The aim of this map was to help planners & decision makers to identify priority area for WASH interventions at Uknia & Teknaf Upazila camps. This map represents the modelled water depth from a 10-year average return interval (ARI) pluvial flood event. Flood depths are derived from hydrodynamic flood modelling.
There are three types of flood at-risk areas has been classified based on depth,
Flood depth low (>=0.10m to 0.5m): impact is likely to be minor
Flood depth moderate (0.5m to 1.0m): need to be combined appropriate protection measures
Flood depth high (>1.0m): people & infrastructures are exposed, the zone should be avoided
Emergency Preparedness: Flood
(Source: Hydrodynamic Modelling v2.1– Deltares/WFP, 2019 for Ukhia Camps, WASH Infrastructures GPS Points: RECAH Coding (2019), WASH Partners & WASH Area Focal Agency (April 07, 2021).